## Slide 1: Legal Definitions of Wetlands
Dani Lay
Adapted from ABE 42600

## Slide 2: Jurisdictional Definition
Wetlands are defined by Section 404 permit of the Clean Water Act (CWA) along with the 1987 Corp of Engineers Wetland Delineation Manual and Regional Supplements
Section 404 permit is needed to place, dredge, or fill materials in “Waters of the United States” (WOTUS)
Three characteristics to determine if an area is a wetland:
1. Hydrophytic vegetation
2. Hydric soils
3. Hydrology

## Slide 3: WOTUS?
WOTUS: connectivity to navigable waters and their ability to protect quality of nearby surface waters
  Navigable waters: “those waters that are subject to the ebb and flow of the tide and/or are presently used, or have been used in the past, or may be susceptible for use to transport interstate or foreign commerce. A determination of navigability, once made, applies laterally over the entire surface of the waterbody, and is not extinguished by later actions or events which impede or destroy navigable capacity.”
CWA left out conversion for agriculture and silviculture
Food Securities Act of 1985 closed the loophole by linking wetland drainage to farm subsidies (i.e., Swampbuster provision)
Federal protection of pocosins, bogs, prairie potholes, and Carolina Bays was often questioned due to the lack of surface connectivity to navigable surface waters
Clean Water Act

## Slide 4: Significant Nexus
Rapanos versus United States yielded a plurality opinion
  Justice Scalia: WOTUS “only if it abuts a tributary with a continuous surface water connection to a traditionally navigable water” [navigable in fact]
  Justice Kennedy: WOTUS “affect the physical, biological, and chemical integrity of downstream navigable water” [significant nexus]
Significant nexus opinion led to the 2015 Clean Water Rule (CWR): case-by-case protection to wetlands that lack surface water connection to navigable waters

## Slide 5: Significant Nexus Determination
RPWs: Relatively permanent waters
TNWs: Traditional navigable waters

## Slide 6: Significant Nexus Determination
Wetlands performing functions that society values…
AND where there is evidence for real potential to affect the physical, chemical, or biological integrity of traditional navigable waters
AND when the evidence is more than speculative or insubstantial

## Slide 7: Significant Nexus Determination
Wetlands performing functions that society values…
AND where there is evidence for real potential to affect the physical, chemical, or biological integrity of traditional navigable waters
AND when the evidence is more than speculative or insubstantial

## Slide 8: Significant Nexus to Navigable In-Fact
Clean Water Rule repealed and replaced with the Navigable Waters Protection Rule (NWPR) in 2020
NWPR put “navigable in-fact” opinion into practice
  Wetlands that do not abut a tributary with continuous or intermittent flow fall outside CWA protection
  ~50% of wetlands would lose CWA protections with NWPR

## Slide 10: U.S. Army Corps of Engineers (USACE) Jurisdictional Wetland Hydrology Definition
Wetland hydrology = inundated or saturated for a sufficient time during the growing season in most years to result in development of hydric soils and dominance by hydrophytic vegetation
  Presence of water has overriding influence on characteristics of vegetation and soil
  12-18 inches from surface, depending on soil type
Focus: dry edge of a wetland to determine wetland extent

## Slide 11: What is not a wetland?
Too dry: Intermittently inundated or saturated for <5% of growing season [soil temperature is >41 °F, approximately the number of frost-free days] (USACE)
Influence of vegetation: 12-18 inches within soil surface
2.5 m depth splits lacustrine and riverine deepwater habitats from wetlands (USFWS National Wetlands Inventory)
5% ranges from 7-18 days depending on region, problematic in some coastal regions
14 days is recommended by National Academy of Sciences

## Slide 12: Wetland Hydrology Indicators
Most reliable evidence: gauging station or groundwater monitoring
Primary indicators: stand-alone evidence of current or recent hydrologic event
Secondary indicators: provide evidence of wetland hydrology when supported by one or more primary or secondary indicators
Groups of Evidence
  Observation of surface water or saturated soils
  Evidence of recent inundation
  Evidence of current or recent soil saturation
  Evidence from other site conditions or data

## Slide 13: Groups A & B
Be aware of recent or unusually high precipitation or drought
Group A: Water table/saturation within 12-18 inches of the soil surface, depending on soil type
FAC-neutral test: >50% of remaining dominant species are FACW and/or OBL; no FAC dominants

## Slide 14: Example Indicators

## Slide 15: Example Indicators

## Slide 16: Groups C & D
Overlap with hydric soil indicators and vegetation indicators
FAC-neutral test: >50% of remaining dominant species are FACW and/or OBL; no FAC dominants

## Slide 17: Example Indicators

## Slide 18: Difficult delineations
Agricultural lands due to lack of native wetland vegetation
Midwest wetlands may lack hydrologic indicators
  Multi-year droughts in a changing climate may mean that a wetland is not saturated or inundated in a given year
  Particularly toward end of growing season

## Slide 19: More ecological view of wetland hydrology
Wetland hydroperiod: seasonal pattern of the water level in a wetland
  Helps characterize type of wetland
  Integrates inflows and outflows
Water levels generally fluctuate
  Seasonally
  Daily or semi-daily
  Unpredictably

## Slide 21: USACE Hydrogeomorphic Classification of Wetlands
Where is the wetland in the landscape?
Where does water come from? Where does water go?
What direction does water flow?
Class | Landscape Position | Dominant Water Source | Dominant Hydrodynamics
Riverine | Adjacent to river/stream | Overbank flow from channel | Unidirectional and horizontal
Depressional | Depressions | Interflow/ groundwater; precipitation | Vertical
Slope | Forced to surface via impermeable layer, sharp slope break, concave land surface | Groundwater | Unidirectional and horizontal
Mineral soil flats | Flat areas | Precipitation | Vertical
Organic soil flats | Flat areas | Precipitation | Vertical
Estuarine fringe | Along an estuary | Overbank from estuary | Bidirectional and horizontal
Lacustrine fringe | Along a lake | Overbank from lake | Bidirectional and horizontal

## Slide 22: Managed Wetland Hydrology
Wetlands for waterfowl
Storage for irrigation
Changing hydroperiod for wetland restorations or natural wetlands
Example Implementation:
Water control structures
Pumping/other diversions
Engineered bypasses for high flow
Levees, embankments, ditches, etc
Notes: Waterfowl impoundment near Pamlico County, NC
Water control structure in the Great Dismal Swamp